# JayBird JCA/JDBC Driver Release Notes v 2.0

## General Notes
JayBird is JCA/JDBC driver suite to connect to Firebird database server. Historically Borland opened sources of type 3 JDBC driver called InterClient. However due to some inherent limitations of Firebird client library it was decided that type 3 driver is a dead end, and Firebird team developed pure Java implementation of wire protocol. This implementation became basis for JayBird, pure Java driver for Firebird relational database.
This driver is based on both the new JCA standard for application server connections to enterprise information systems and the well known JDBC standard. The JCA standard specifies an architecture in which an application server can cooperate with a driver so that the application server manages transactions, security, and resource pooling, and the driver supplies only the connection functionality. While similar to the JDBC 2 XADataSource idea, the JCA specification is considerably clearer on the division of responsibility between the application server and driver.
### Supported Firebird versions
JayBird 2.0 supports Firebird 1.0.x SuperServer and Classic, Firebird 1.5 SuperServer and Classic independently of the platform on which server runs when type 4 JDBC driver is used. Type 2 and embedded server JDBC drivers require JNI library, precompiled binaries for Win32 and Linux platforms are shipped in the default installation, other platforms require porting/building JNI library for that platform. Driver no longer supports InterBase servers due to a Firebird-specific changes in database attachment parameters that are send to the server.
### Specification support
Driver supports following specifications:
JDBC 3.0	Driver passed complete JDBC compatibility test suite, though some features are not implemented. It is not officially JDBC compliant, because of high certification costs.
JDBC 2.0 Standard Extensions	JayBird provides implementation of following interfaces from javax.sql.* package: / ConnectionPoolDataSource implementation provides connection and prepared statement pooling. / DataSource implementation provides seamless integration with major web and application servers. / XADataSource implementation provides means to use driver in distributed transactions.
JCA 1.0	JayBird provides implementation of javax.resource.spi.ManagedConnectionFactory and related interfaces. CCI interfaces are not supported.
JTA 1.0.1	Driver provides implementation of javax.transaction.xa.XAResource interface via JCA framework and XADataSource implementation.
JMX 1.2	JayBird 2.0 provides MBean to manage Firebird server and installed databases via JMX agent.

## What's new in JayBird 2.0
JayBird 2.0 underwent significant internal changes that are not directly visible to the client code, and not necessarily introduced new features. However those changes significantly increase code modularity, stability and maintainability.
### Refactorings
- Significant refactoring of the org.firebirdsql.gds.* package. Implementations of the interfaces defined in this package are now dynamically loaded from the classpath and provide possibilities to extend driver with custom code without changing the driver itself.
- JCA code was significantly changed, bringing a long awaited stability when critical errors happen into that vital part of code. There is no more so-called “fatal” errors that can cause driver to recycle connections and transactions.
- Refactoring of the transaction and object life-cycle management in the JDBC code. Main reason for this change was the need to remove result set caching in auto-commit mode and make it JDBC specification compliant, but it has also positive effect on the code stability and maintainability.
- Unified connection property handling in JCA, driver manager and pooling code. This solves a longstanding issue which caused configuration
- Refactorings to support JDK 5.0.
### Updatable result sets
JayBird 2.0 provides now support for the updatable result sets. Feature allows Java application to update current record using the updateXXX methods of java.sql.ResultSet interface. Updates are performed within the current transaction using a best row identifier in WHERE clause. This sets the following limitation on the result set “updatability”:
- the SELECT references single table;
- all columns not referenced in SELECT permit NULLs (otherwise INSERTs will fail);
- the SELECT statement does not contain DISTINCT predicate, aggregate functions, joined tables or stored procedures;
- the SELECT statement references all columns from the table primary key definition or an RDB$DB_KEY column.
### Firebird management interfaces
JayBird 2.0 provides full support of the Firebird Services API that allows Java applications to perform various server management tasks:
- database backup/restore on remote server; it is possible to performs metadata-only backups, switch the garbage collection during backup off, restore databases with no validity constraints or active indices, etc.
- database maintenance, e.g. database shutdown, sweep, changing the forced writes settings, changing SQL dialect of the database, shadow management, etc.
- retrieving database statistics including header page statistics, system table statistics, data page statistics and index statistics.
- user management, including adding, modifying, and deleting user accounts.
### Incompatible changes since JayBird 2.0
- Signatures of all org.firebirdsql.gds.* classes have changed. This was done in preparation of the official Firebird Java API. After the API release all signature changes will be frozen and correctly versioned.
- FirebirdConnection.getBlob() method signature changed to return java.sql.Blob, previously it returned org.firebirdsql.jdbc.FirebirdBlob. Object that is returned can safely be casted to org.firebirdsql.jdbc.FirebirdBlob interface. The change is caused by the forthcoming JDBC 4.0 specification to avoid conflict in next versions.
- JayBird 1.x allowed to execute queries in auto-commit mode, loop through the obtained result set and to execute other statements through the same connection. This is no longer possible in JayBird 2.0 without changing the result set holdability. The behavior was changed in order to conform the JDBC 3.0 specification, chapter 10.1 “Transaction Boundaries and Auto-commit”. Applications willing to use this feature have to set the result set holdability to ResultSet.HOLD_CURSORS_OVER_COMMIT. Please note, that this option assumes that result set type is TYPE_SCROLL_INSENSITIVE and is completely cached on the client side.
### JayBird JDBC extensions
JayBird 2.0 provides extensions to some JDBC interfaces. JDBC extension interface classes are released under modified BSD license, on “AS IS” and “do what you want” basis, this should make linking to these classes safe from the legal point of view. All classes belong to org.firebirdsql.jdbc.* package. Table below shows all JDBC extensions present in JayBird with a driver version in which the extension was introduced.
JayBird 2.0 JDBC extensions
Interface	Since	Method name	Description
FirebirdDriver	2.0	newConnectionProperties()	Create new instance of FirebirdConnectionProperties interface that can be used to set connection properties programmatically.
		connect(FirebirdConnectionProperties)	Connect to the Firebird database using the specified connection properties.
FirebirdConnectionProperties	2.0	see JDBC connection properties section for more details.
FirebirdConnection	1.5	createBlob()	Create new BLOB in the database. Later this BLOB can be passed as a parameter into PreparedStatement or CallableStatement.
	1.5	getIscEncoding()	Get connection character encoding.
	2.0	getTransactionParameters( int isolationLevel )	Get the TPB parameters for the specified transaction isolation level.
	2.0	createTransactionParameterBuffer()	Create an empty transaction parameter buffer.
	2.0	setTransactionParameters( int isolationLevel, TransactionParameterBuffer tpb )	Set TPB parameters for the specified transaction isolation level. The newly specified mapping is valid for the whole connection lifetime.
	2.0	setTransactionParameters( TransactionParameterBuffer tpb )	Set TPB parameters for the specified transaction isolation level. The newly specified parameters are effective until the transaction isolation is changed.
FirebirdDatabaseMetaData		getProcedureSourceCode(String)	Get source code for the specified stored procedure name.
		getTriggerSourceCode(String)	Get source code for the specified trigger name.
		getViewSourceCode(String)	Get source code for the specified view name.
FirebirdStatement	1.5	getInsertedRowsCount() getUpdatedRowsCount() getDeletedRowsCount()	Extension that allows to get more precise information about outcome of some statement.
	1.5	hasOpenResultSet()	Check if this statement has open result set. Correctly works only when auto-commit is disabled. Check method documentation for details.
	1.5	getCurrentResultSet()	Get current result set. Behaviour of this method is similar to the behavior of the Statement.getResultSet(), except that this method can be called as much as you like.
	1.5	isValid()	Check if this statement is still valid. Statement might be invalidated when connection is automatically recycled between transactions due to some irrecoverable error.
	2.0	getLastExecutionPlan()	Get execution plan for the last executed statement.
FirebirdPreparedStatement	2.0	getExecutionPlan()	Get the execution plan of this prepared statement.
	2.0	getStatementType()	Get the statement type of this prepared statement.
FirebirdCallableStatement	1.5	setSelectableProcedure( boolean selectable )	Mark this callable statement as a call of the selectable procedure. By default callable statement uses "EXECUTE PROCEDURE" SQL statement to invoke stored procedures that return single row of output parameters or a result set. In former case it retrieves only the first row of the result set.
FirebirdResultSet	2.0	getExecutionPlan()	Get execution plan for this result set.
FirebirdBlob	1.5	detach()	Method “detaches” a BLOB object from the underlying result set. Lifetime of “detached” BLOB is limited by the lifetime of the connection.
	1.5	isSegmented()	Check if this BLOB is segmented. Seek operation is not defined for the segmented BLOBs.
	1.5	setBinaryStream( long position )	Opens an output stream at the specified position, allows modifying BLOB content. Due to server limitations only position 0 is supported.
FirebirdBlob.BlobInputStream	1.5	getBlob()	Get corresponding BLOB instance.
	1.5	seek(int position)	Change the position from which BLOB content will be read, works only for stream BLOBs.
FirebirdSavepoint	2.0	interface is equivalent to the java.sql.Savepoint interface introduced in JDBC 3.0 specification, however allows using Firebird savepoints also in JDBC 2.0 (JDK 1.3.x) applications.

### JDBC 3.0 compatibility
JayBird 2.0 includes number of fixes that allow it pass JDBC 3.0 compatibility suite. It successfully passes 1216 tests, 60 tests were excluded, because they are either not applicable to Firebird or fail due to some server problems (math rounding issues, limitations of NUMERIC data type, etc.).
## Distribution package
JayBird driver has compile-time and run-time dependencies to JCA 1.0, JTA 1.0.1, JAAS 1.0 and JDBC 2.0 Optional Package. Additionally, if Log4J classes are found in the class path, it is possible to enable extensive logging inside the driver.
Following file groups can be found in distribution package:
- jaybird-2.0.0.jar – archive containing JCA/JDBC driver and JMX management class. It requires JCA 1.0, JTA 1.0.1, and JAAS 1.0.
- jaybird-pool-2.0.0.jar – archive contains implementation of connection pooling and statement pooling interfaces.
- jaybird-full-2.0.0.jar – merge of firebirdsql.jar and mini-j2ee.jar. This archive can be used for standalone[1] JayBird deployments.
  [1] You have to ensure that your class path contains JAAS 1.0 classes when using JDK 1.3.x.
- jaybird-2.0.0.rar – resource archive ready for deployment in JCA-enabled application servers.
- lib/jaas.jar – archive containing JAAS 1.0 classes.
- lib/log4j-core.jar – archive containing core Log4J classes that provide a possibility to log into the file.
- lib/mini-j2ee.jar – archive containing JCA 1.0, JTA 1.0.1 and JDBC 2.0 Optional Package classes.
- jaybird2.dll – Windows version of the JNI library for Type 2 and Embedded Server drivers.
- libjaybird2.so – Linux version of the JNI library for Type 2 and Embedded Server drivers.
### License
JayBird JCA/JDBC driver is distributed under the GNU Lesser General Public License (LGPL). Text of the license can be obtained from http://www.gnu.org/copyleft/lesser.html. Using JayBird (by importing JayBird's public interfaces in your Java code), and extending JayBird by subclassing or implemention of an extension interface (but not abstract or concrete class) is considered by the authors of JayBird to be dynamic linking. Hence our interpretation of the LGPL is that the use of the unmodified JayBird source does not affect the license of your application code.
Even more, all extension interfaces to which application might want to link are released under dual LGPL/modified BSD license. Latter is basically “AS IS” license that allows any kind of use of that source code. JayBird should be viewed as an implementation of that interfaces and LGPL section for dynamic linking is applicable in this case.
### Source Code
Source code can be obtained from the CVS at SourceForge.net. The CVSROOT is
:pserver:anonymous@cvs.sourceforge.net:/cvsroot/firebird, the module name is client-java. Alternatively source code can be viewed online at http://cvs.sourceforge.net/viewcvs.py/firebird/client-java/
## JDBC URL Format
Driver provides different JDBC URLs for different usage scenarios:
### Pure Java
jdbc:firebirdsql:host[/port]:/path/to/db.fdb
jdbc:firebirdsql://host[:port]/path/to/db.fdb
Default URL, will connect to the database using type 4 JDBC driver. Best suited for client-server applications with dedicated database server. Port can be omitted (default value is 3050), host name must be present.
First format is considered official, second – compatibility mode for InterClient migration.
### Using Firebird client library
jdbc:firebirdsql:native:host[/port]:/path/to/db.fdb jdbc:firebirdsql:native://host[:port]/path/to/db.fdb
Type 2 driver, will connect to the database using client library (either fbclient.dll or gds32.dll on Windows, and libfbclient.so or libgds.so on Linux). Requires correct installation of the client library.
jdbc:firebirdsql:local:/path/to/db.fdb
Type 2 driver in local mode. Uses client library as in previous case, however will not use socket communication, but rather access database directly. Requires correct installation of the client library.
### Embedded Server
jdbc:firebirdsql:embedded:/path/to/db.fdb
Similar to the Firebird client library, however fbembed.dll on Windows and libfbembed.so on Linux are used. Requires correctly installed and configured Firebird embedded server.
## JDBC connection properties
Table below contains properties that specify parameters of the connections that are obtained from this data source. Commonly used parameters have the corresponding getter and setter methods, rest of the Database Parameters Block parameters can be set using setNonStandardProperty setter method.
Property	Getter	Setter	Description
database	+	+	Path to the database in the format / [host/port:]/path/to/database.fdb
type	+	+	Type of the driver to use. Possible values are: / PURE_JAVA or TYPE4 for type 4 JDBC driver / NATIVE or TYPE2 for type 2 JDBC driver / EMBEDDED for using embedded version of the Firebird.

blobBufferSize	+	+	Size of the buffer used to transfer BLOB content. Maximum value is 64k-1.
socketBufferSize	+	+	Size of the socket buffer. Needed on some Linux machines to fix performance degradation.
buffersNumber	+	+	Number of cache buffers (in database pages) that will be allocated for the connection. Makes sense for ClassicServer only.

charSet	+	+	Character set for the connection. Similar to encoding property, but accepts Java names instead of Firebird ones.
encoding	+	+	Character encoding for the connection. See Firebird documentation for more information.
useTranslation	+	+	Path to the properties file containg character translation map.

password	+	+	Corresponding password.
roleName	+	+	SQL role to use.
userName	+	+	Name of the user that will be used by default.

useStreamBlobs	+	+	Boolean flag tells driver whether stream BLOBs should be created by the driver, by default “false”. Stream BLOBs allow “seek” operation to be called, however due to a bug in gbak utility they are disabled by default.
useStandardUdf	+	+	Boolean flag tells driver to assume that standard UDFs are defined in the database. This extends the set of functions available via escaped function calls. This does not affect non-escaped use of functions.

tpbMapping	+	+	TPB mapping for different transaction isolation modes.
defaultIsolation	+	+	Default transaction isolation level. All newly created connections will have this isolation level. One of: / TRANSACTION_READ_COMMITTED / TRANSACTION_REPEATABLE_READ / TRANSACTION_SERIALIZABLE
defaultTransactionIsolation	+	+	Integer value from java.sql.Connection interface corresponding to the transaction isolation level specified in isolation property.

nonStandardProperty	getNonStandardProperty(String)	+ / setNonStandardProperty(String) / setNonStandardProperty(String, String)	Allows to set any valid connection property that does not have corresponding setter method. Two setters are available: / setNonStandardProperty(String) method takes only one parameter in form “propertyName[=propertyValue]”, this allows setting non-standard parameters using configuration files. / setNonStandardProperty(String, String) takes property name as first parameter, and its value as the second parameter.

## Using Type 2 and Embedded Server driver
JayBird 2.0 provides type 2 JDBC driver that uses native client library to connect to the databases. Additionally JayBird 2.0 can use embedded version of Firebird relational database allowing to create Java applications that does not require separate server setup.
However type 2 driver has also limitations:
- Due to multi-threading issues in Firebird client library as well as in embedded server version, it is not possible to access them from different threads simultaneously. When using client library only one thread is allowed to access connection at a time, however it is allowed to access different connections from different threads. Client library in local mode and embedded server library on Linux do not allow multithreaded access to the library. JayBird provides necessary synchronization in Java code, however corresponding mutex is local to the classloader that loaded JayBird driver. Care should be taken when deploying applications in web or application servers: put jar files in the main library directory of the web and/or application server, not in the library directory of the web or enterprise application (WEB-INF/lib directory or in the .EAR file). This issue will be fixed in Firebird client library after merge with Vulcan project.
- Current implementation of the JNI library allows that either client library or embedded server library is loaded into memory. The first library being loaded wins, attempt to load second library will produce an error. Usually this is not a problem, since embedded server library can also act as a client library, so it is enough to load embedded server library first. This limitation will be removed in JayBird 2.1, implementation already exists, however it was contributed already at RC stage; adding it to the release would delay it for few months.
### Configuring Type 2 JDBC driver
Type 2 JDBC driver requires JNI library to be installed and available for Java Virtual Machine. Precompiled binaries for Windows and Linux platforms are distributed with JayBird:
- jaybird2.dll is precompiled binary for Windows platform. Successfully tested with Windows 2000 and Windows XP SP1, but there should be no issues also in other Win32 OS.
  Library should be either copied into the directory specified in %PATH% environment variable, or made available to JVM using the java.library.path system property.
- libjaybird2.so is precompiled binary for Linux platform. It must be available via the LD_LIBRARY_PATH environment variable, e.g. copied into /usr/lib/ directory. Another possibility is to specify path to the directory with JayBird JNI library in java.library.path system property during the JVM startup.
- Other platforms can easily compile the JNI library by checking out the JayBird sources from the CVS and using “./build.sh compile-native” command in the directory with checked out sources.
After making JayBird JNI library available to the JVM application has to tell driver to start using this by either specifying TYPE2 or LOCAL type in the connection pool or data source properties or using appropriate JDBC URL when connecting via java.sql.DriverManager.
### Configuring Embedded Server JDBC driver
Embedded Server JDBC driver uses same JNI library and configuration steps for the type 2 JDBC driver.
There is however one issue related to the algorithm of Firebird Embedded Server installation directory resolution. Firebird server uses pluggable architecture for internationalization. By default server loads fbintl.dll or libfbintl.so library that contains various character encodings and collation orders. This library is expected to be installed in the intl/ subdirectory of the server installation. The algorithm of directory resolution is the following:
1. FIREBIRD environment variable.
2. RootDirectory parameter in the firebird.conf file.
3. The directory where server binary is located.
When Embedded Server is used from Java and no FIREBIRD environment variable is specified, it tries to find firebird.conf in the directory where application binary is located. In our case application binary is JVM and therefore Embedded Server tries to find its configuration file in the bin/ directory of the JDK or JRE installation. Same happens to the last item of the list. In most cases this is not desired behavior.
Therefore, if application uses character encodings, UDFs or wants to fine-tune server's behavior through the configuration file, the FIREBIRD environment variable must be specified and point to the installation directory of the Embedded Server, e.g. current working directory.
## JDBC 3.0 Compatibility
As it was mentioned before, JayBird 2.0 JCA/JDBC driver passed Sun JDBC CTS 1.3.1 test suite. All tests except those that do not apply to Firebird RDBMS succeeded. However driver is not officially JDBC-compliant because certification procedure is too expensive.
### JDBC 3.0 deviations and unimplemented features
The following optional features and the methods for their support are not implemented:
- java.sql.Array data type is not yet supported.
- java.sql.Blob does not implement following methods:
  - position(Blob, long) and position(byte[], long); Firebird does not provide any server-side optimization for these calls, client application must fetch complete BLOB content from the server to do pattern search.
  - truncate(long); Firebird does not provide such functionality on the server side, application must fetch old BLOB from the server and pump old content into a newly created BLOB.
- java.sql.Clob data type is not yet supported.
- java.sql.Connection
  - getCatalog() and setCatalog(String) are not supported by Firebird server.
  - getTypeMap() and setTypeMap(Map) are not supported.
  - prepareStatement(String, int), prepareStatement(String, int[]) and prepareStatement(String, String[]) that return auto-generated keys are not implemented, because this functionality is not provided by server.
- java.sql.PreparedStatement
  - setObject(int index, Object object, int type) Target SQL type is determined from the class of the passed object and corresponding parameter is ignored.
  - setObject(int index, Object object, int type, int scale) Same as above, type and scale are ignored.
- java.sql.Ref data type is not supported by Firebird server.
- java.sql.SQLData data type is not supported by Firebird server.
- java.sql.SQLInput is not supported.
- java.sql.SQLOutput is not supported.
- java.sql.Statement
  - cancel() is not supported by Firebird server.
  - execute(String, int), execute(String, int[]), execute(String, String[]), executeUpdate(String, int), executeUpdate(String, int[]), and executeUpdate(String, String[]) that return auto-generated keys are not implemented, because of server incapability.
  - getGeneratedKeys() is not implemented because server does not support this feature yet. As soon as support for this feature is available, driver will be updated.
- java.sql.Struct data type is not supported by server.
The following methods are implemented, but deviate from the specification:
- java.sql.Statement
  - get/setMaxFieldSize does nothing, Firebird server does not support this feature.
  - get/setQueryTimeout does nothing, Firebird server does not support this feature.
- java.sql.PreparedStatement
  - setObject(int index, Object object, int type) Target SQL type is determined from the class of the passed object and corresponding parameter is ignored.
  - setObject(int index, Object object, int type, int scale) Same as above, type and scale are ignored.
- java.sql.ResultSetMetaData
  - isReadOnly() always returns false
  - isWritable() always returns true
  - isDefinitivelyWritable() always returns true
## JayBird Specifics
JayBird driver has also some implementation-specific issues that should be considered during development.
### Result sets
JayBird behaves differently not only when different result set types are used but also the behavior depends whether connection is in auto-commit mode or not.
ResultSet.TYPE_FORWARD_ONLY result sets when used in auto-commit mode are completely cached on the client before the execution of the query is finished. This leads to the increased time needed to execute statement, however the result set navigation happens almost instantly. When auto-commit mode is switched off, only part of the result set specified by the fetch size is cached on the client.
ResultSet.TYPE_SCROLL_INSENSITIVE result sets are always cached on the client. The reason is quite simple – Firebird API does not provide scrollable cursor support, navigation is possible only in one direction.
ResultSet.HOLD_CURSORS_OVER_COMMIT holdability is supported in JayBird only for result sets of type ResultSet.TYPE_SCROLL_INSENSITIVE. For other result set types driver will throw an exception.
### Using java.sql.ParameterMetaData with Callable Statements
This interface can be used only to obtain information about the IN parameters. Also it is not allowed to call the PreparedStatement.getParameterMetaData method before all of the OUT parameters are registered. Otherwise the corresponding method of CallableStatement throws an SQLException, because the driver tries to prepare the procedure call with incorrect number of parameters.
### Using ResultSet.getCharacterStream with BLOB fields
JayBird JDBC driver always uses connection encoding when converting array of bytes into character stream. The BLOB SUB_TYPE 1 fields allow setting the character encoding for the field. However when the contents of the field is sent to the client, it is not converted according to the character set translation rules in Firebird, but is sent “as is”. When such field is accessed from Java application via JayBird and character set of the connection does not match the character encoding of the field, conversion errors might happen. Therefore it is recommended to convert such fields in the application using the appropriate encoding.
## Connection pooling with JayBird 2.0
Connection pooling provides effective way to handle physical database connections. It is believed that establishing new connection to the database takes some noticeable amount or time and in order to speed things up one has to reuse connections as much as possible. While this is true for some software and for old versions of Firebird database engine, establishing connection is hardly noticeable with Firebird 1.0.3 and Firebird 1.5. So why is connection pooling needed?
There are few reasons for this. Each good connection pool provides a possibility to limit number of physical connections established with the database server. This is an effective measure to localize connection leaks. Any application cannot open more physical connections to the database than allowed by connection pool. Good pools also provide some hints where connection leak occurred. Another big advantage of connection pool is that it becomes a central place where connections are obtained, thus simplifying system configuration. However, main advantage of good connection pool comes from the fact that in addition to connection pooling, it can pool also prepared statement. Tests executed using AS3AP benchmark suite show that prepared statement pooling might increase speed of the application by 100% keeping source code clean and understandable.
### Usage scenario
When some statement is used more than one time, it makes sense to use prepared statement. It will be compiled by the server only once, but reused many times. It provides significant speedup when some statement is executed in a loop. But what if some prepared statement will be used during lifetime of some object? Should we prepare it in object's constructor and link object lifetime to JDBC connection lifetime or should we prepare statement each time it is needed? All such cases make handling of the prepared statements hard, they pollute application's code with irrelevant details.
Connection and statement pooling remove such details from application's code. How would the code in this case look like? Here's the example
Example 1. Typical JDBC code with statement pooling
001 / 002 / 003 / 004 / 005 / 006 / 007 / 008 / 009 / 010 / 011 / 012 / 013 / 014 / 015 / 016 017 018	... / Connection connection = dataSource.getConnection(); / try { / PreparedStatement ps = connection.prepareStatement( / “SELECT * FROM test_table WHERE id = ?”); / try { / ps.setInt(1, id); / ResultSet rs = ps.executeQuery(); / while (rs.next()) { / // do something here / } / } finally { / ps.close(); / } / } finally { / connection.close(); / } / ...

Lines 001-018 show typical code when prepared statement pooling is used. Application obtains JDBC connection from the data source (instance of javax.sql.DataSource interface), prepares some SQL statement as if it is used for the first time, sets parameters, and executes the query. Lines 012 and 015 ensure that statement and connection will be released under any circumstances. Where do we benefit from the statement pooling? Call to prepare a statement in lines 004-005 is intercepted by the pool, which checks if there's a free prepared statement for the specified SQL query. If no such statement is found it prepares a new one. In line 013 prepared statement is not closed, but returned to the pool, where it waits for the next call. Same happens to the connection object that is returned to the pool in line 016.
### Connection Pool Classes
JayBird 2.0 connection pooling classes belong to org.firebirdsql.pool.* package.
Description of some connection pool classes.
AbstractConnectionPool	Base class for all connection pools. Can be used for implementing custom pools, not necessarily for JDBC connections.
BasicAbstractConnectionPool	Subclass of AbstractConnectionPool, implements javax.sql.ConnectionPoolDataSource interface. Also provides some basic properties (minimum and maximum number of connections, blocking and idle timeout, etc) and code to handle JNDI-related issues.
DriverConnectionPoolDataSource	Implementation of javax.sql.ConnectionPoolDataSource for arbitrary JDBC drivers, uses java.sql.DriverManager to obtain connections, can be used as JNDI object factory.
FBConnectionPoolDataSource	JayBird specific implementation of javax.sql.ConnectionPoolDataSource and javax.sql.XADataSource interfaces, can be used as JNDI object factory.
FBSimpleDataSource	Implementation of javax.sql.DataSource interface, no connection and statement pooling is available, connections are physically opened in getConnection() method and physically closed in their close() method.
FBWrappingDataSource	Implementation of javax.sql.DataSource interface that uses FBConnectionPoolDataSource to allocate connections. This class defines some additional properties that affect allocated connections. Can be used as JNDI object factory.
SimpleDataSource	Implementation of javax.sql.DataSource interface that uses javax.sql.ConnectionPoolDataSource to allocate physical connections.

### org.firebirdsql.pool.FBConnectionPoolDataSource
This class is a corner stone of connection and statement pooling in JayBird. It can be instantiated within the application as well as it can be made accessible to other applications via JNDI. Class implements both java.io.Serializable and javax.naming.Referenceable interfaces, which allows using it in a wide range of web and application servers.
Class implements both javax.sql.ConnectionPoolDataSource and javax.sql.XADataSource interfaces. Pooled connections returned by this class implement javax.sql.PooledConnection and javax.sql.XAConnection interfaces and can participate in distributed JTA transactions.
Class provides following configuration properties:
Standard JDBC Properties
This group contains properties defined in the JDBC specification and should be standard to all connection pools.
Property	Getter	Setter	Description
maxIdleTime	+	+	Maximum time in milliseconds after which idle connection in the pool is closed.
maxPoolSize	+	+	Maximum number of open physical connections.
minPoolSize	+	+	Minimum number of open physical connections. If value is greater than 0, corresponding number of connections will be opened when first connection is obtained.
maxStatements	+	+	Maximum size of prepared statement pool. If 0, statement pooling is switched off. When application requests more statements than can be kept in pool, JayBird will allow creating that statements, however closing them would not return them back to the pool, but rather immediately release the resources.

Pool Properties
This group of properties are specific to the JayBird implementation of the connection pooling classes.
Property	Getter	Setter	Description
blockingTimeout	+	+	Maximum time in milliseconds during which application can be blocked waiting for a connection from the pool. If no free connection can be obtained, exception is thrown.
retryInterval	+	+	Period in which pool will try to obtain new connection while blocking the application.
pooling	+	+	Allows to switch connection pooling off.
statementPooling	+	+	Allows to switch statement pooling off.
pingStatement	+	+	Statement that will be used to “ping” JDBC connection, in other words, to check if it is still alive. This statement must always succeed.
pingInterval	+	+	Time during which connection is believed to be valid in any case. Pool “pings” connection before giving it to the application only if more than specified amount of time passed since last “ping”.

Runtime Pool Properties
This group contains read-only properties that provide information about the state of the pool.
Property	Getter	Setter	Description
freeSize	+	-	Tells how many free connections are in the pool. Value is between 0 and totalSize.
workingSize	+	-	Tells how many connections were taken from the pool and are currently used in the application.
totalSize	+	-	Total size of open connection. At the pool creation – 0, after obtaining first connection – between minPoolSize and maxPoolSize.
connectionCount	+	-	Deprecated. Same as freeSize.

### org.firebirdsql.pool.FBWrappingDataSource
This class is a wrapper for FBConnectionPoolDataSource converting interface from javax.sql.ConnectionPoolDataSource to javax.sql.DataSource. It defines same properties as FBConnectionPoolDataSource does.
### Runtime object allocation and deallocation hints
Pool implementation shipped with JayBird can provide hints for the application where the connection was obtained from the pool, when it was released back to the pool, when the statement was prepared. Such information is written into the log when appropriate system properties are set to true. Additionally, when connection or prepared statement is closed twice, driver will throw an SQL exception with an attached stack trace of previous call to close() method.
List of properties
Property name	Description
FBLog4j	Enables logging inside driver. This is the essential property, if it is not present or set to false, no debug information is available. / When it is set to true, pool automatically prints the following information: / When physical connection is added to the pool – DEBUG / When a maximum pool capacity is reached – DEBUG / When connection is obtained from pool – DEBUG / When connection is released back to pool – DEBUG / Whether pool supports open statements across transaction boundaries – INFO
FBPoolShowTrace	Enables logging of the thread stack trace when debugging is enabled and: / Connection is allocated from the pool – DEBUG / Thread is blocked while waiting for a free connection – WARN
FBPoolDebugStmtCache	When statement caching is used and debugging is enabled, following information is logged: / When a statement is prepared – INFO / When statement cache is cleaned – INFO / When statement is obtained from or returned back to pool – INFO

## Documentation and Support
### Where to get more information on JayBird
The most detailed information can be found in the JayBird Frequently Asked Questions (FAQ). The FAQ is included in the distribution, and is available on-line in several places.
Also a new resource, JayBirdWiki is available at http://jaybirdwiki.firebirdsql.org.
### Where to get help
The best place to start is the FAQ. Many details for using JayBird with various programs are located there. Below are some links to useful web sites.
- The http://groups.yahoo.com/group/Firebird-Java and corresponding mailing list Firebird-Java@yahoogroups.com.
- The code for Firebird and this driver are on http://sourceforge.net/projects/firebird.
- The Firebird project home page http://www.firebirdsql.com.
### Reporting Bugs
The developers follow the Firebird-Java@yahoogroups.com list. Join the list and post information about suspected bugs. This is a good idea because what is often thought to be a bug turns out to be something else. List members may be able o help out and get you going again, whereas bug fixes might take awhile.
If you are sure that this is a bug you may report it in the Firebird bug tracker, “Java Client (JayBird)” at SourceForge.net project area (http://sourceforge.net/projects/firebird).
### Corrections/Additions To Release Notes
Please send corrections, suggestions, or additions to these Release Notes to to the mailing list at Firebird-Java@yahoogroups.com.