# JCA/JDBC Driver Release Notes v 2.3.0

## General Notes
Jaybird is a JCA/JDBC driver suite to connect to Firebird database servers.
This driver is based on both the JCA standard for application server connections to enterprise information systems and the well-known JDBC standard. The JCA standard specifies an architecture in which an application server can cooperate with a driver so that the application server manages transactions, security, and resource pooling, and the driver supplies only the connection functionality. While similar to the JDBC XADataSource concept, the JCA specification is considerably clearer on the division of responsibility between the application server and driver.
### Supported Firebird versions
Jaybird 2.3.0 was tested against Firebird 2.1.5 and 2.5.2, but should also support other Firebird versions from 2.0 and up. Formal support for Firebird 1.x has been dropped (although in general we expect the driver to work). The Type 2 and embedded server JDBC drivers require the appropriate JNI library. Pre-compiled JNI binaries for Win32 and Linux platforms are shipped in the default installation, other platforms require porting/building the JNI library for that platform.
This driver does not supports InterBase servers due to Firebird-specific changes in the protocol and database attachment parameters that are sent to the server.
### Supported Java versions
Jaybird 2.3.0 supports Java 6 (JDBC 4.0) and Java 7 (JDBC 4.1). Support for earlier Java versions has been dropped.
### Specification support
Driver supports the following specifications:
JDBC 4.1	Driver implements all JDBC 4.1 methods added to existing interfaces. The driver explicitly supports closeOnCompletion, most other JDBC 4.1 specific methods throw SQLFeatureNotSupportedException.
JDBC 4.0	Driver implements all JDBC 4.0 interfaces and supports exception chaining.
JCA 1.0	Jaybird provides implementation of javax.resource.spi.ManagedConnectionFactory and related interfaces. CCI interfaces are not supported. / Although Jaybird depends on the JCA 1.5 classes, JCA 1.5 compatibility is currently not guaranteed.
JTA 1.0.1	Driver provides an implementation of javax.transaction.xa.XAResource interface via JCA framework and XADataSource implementation.
JMX 1.2	Jaybird provides a MBean to manage Firebird servers and installed databases via JMX agent.

## What's new in Jaybird 2.3
Jaybird 2.3 introduces the following new features and fixes:
### Removal of deprecated classes, packages and methods
See Removal of deprecated classes, packages and methods inCompatibility changes for more details.
### Other fixes and changes
Fix: IP-address is reversed on big-endian platforms(JDBC-98)
A full list of changes is available at:
http://tracker.firebirdsql.org/secure/ReleaseNote.jspa?version=10440&styleName=Text&projectId=10002&Create=Create
## Compatibility changes
Jaybird 2.3 introduces some changes in compatibility and announces future breaking changes.
### Stricter JDBC compliance
In Jaybird 2.3 a number of changes were made for stricter compliance to the JDBC specification
### Removal of deprecated classes, packages and methods
DataSource and connection pooling
The classes in org.firebirdsql.pool and org.firebirdsql.pool.sun have been removed completely, with the exception of org.firebirdsql.pool.FBSimpleDataSource. This class has been moved to org.firebirdsql.ds.FBSimpleDataSource. A subclass with the same name is kept in org.firebirdsql.pool for backwards compatibility. This subclass will be removed in future versions of Jaybird.
With this change, there are no DataSource implementations in Jaybird to provide connection pooling (the ConnectionPoolDataSource implementations are for use by a connection pool and not a connection pool themselves). Either use the connection pool provided by your Application Server, or use a third-party connection pool like c3p0, Apache DBCP or BoneCP.
The class org.firebirdsql.jca.FBXADataSource has been removed as well. Its replacement is org.firebirdsql.ds.FBXADataSource (which was introduced in Jaybird 2.2).
FirebirdSavepoint
All method definitions in the interface org.firebirdsql.jdbc.FirebirdSavepoint were removed, and methods referencing this interface in org.firebirdsql.jdbc.FirebirdConnection have been removed as the interface duplicated the java.sql.Savepoint interface and related methods in java.sql.Connection. The interface itself remains for potential future Firebird-specific extensions.
### Breaking changes for Jaybird 3.0
With Jaybird 3.0 the following breaking changes will be introduced.
Dropping support for Java 6
Jaybird 3.0 will drop support for Java 6, as Java 6 has gone end-of-public-updates in February, 2013[1].
[1] See the Java SE EOL policy on http://www.oracle.com/technetwork/java/eol-135779.html
## Distribution package
The following file groups can be found in distribution package:
- jaybird-2.3.0.jar – archive containing JCA/JDBC driver, implementation of connection pooling and statement pooling interfaces, and JMX management class. It requires JCA 1.5
- jaybird-full-2.3.0.jar – merge of jaybird-2.3.0.jar and connector-api-1.5.jar. This archive can be used for standalone Jaybird deployments
- jaybird-2.3.0-sources.jar – archive containing the sources of Jaybird (specific to this JDK version); for including Jaybird sources in your IDE
- lib/connector-api-1.5.jar – archive containing JCA 1.5 classes (required dependency)
- lib/antlr-runtime-3.4.jar – archive containing ANTLR runtime classes, required for generated keys functionality (optional dependency)
- lib/log4j-core.jar – archive containing core Log4J classes that provide logging (optional dependency)
Jaybird has compile-time and run-time dependencies to the JCA 1.5 classes. Additionally, if Log4J classes are found in the class path, it is possible to enable extensive logging inside the driver. If the ANTLR runtime classes are absent, the generated keys functionality will not be available.
Native dependencies (required only for Type 2 and Embedded):
- jaybird23.dll – Windows 32-bit
- jaybird23_x64.dll – Windows 64-bit
- libjaybird23.so – Linux 32-bit (x86)
- libjaybird23_x64.so – Linux 64-bit (AMD/Intel 64)
The Windows DLLs have been built with Microsoft Visual Studio 2010 SP1. To use the native or embedded driver, you will need to install the Microsoft Visual C++ 2010 SP 1 redistributable available at:
- x86: http://www.microsoft.com/download/en/details.aspx?id=8328
- x64: http://www.microsoft.com/download/en/details.aspx?id=13523
### License
Jaybird JCA/JDBC driver is distributed under the GNU Lesser General Public License (LGPL). Text of the license can be obtained from http://www.gnu.org/copyleft/lesser.html.
Using Jaybird (by importing Jaybird's public interfaces in your Java code), and extending Jaybird by subclassing or implementation of an extension interface (but not abstract or concrete class) is considered by the authors of Jaybird to be dynamic linking. Hence our interpretation of the LGPL is that the use of the unmodified Jaybird source does not affect the license of your application code.
Even more, all extension interfaces to which application might want to link are released under dual LGPL/modified BSD license. Latter is basically “AS IS” license that allows any kind of use of that source code. Jaybird should be viewed as an implementation of that interfaces and LGPL section for dynamic linking is applicable in this case.
### Source Code
The distribution package contains the normal sources in jaybird-2.2.0-sources.jar; this file does not include the sources of the tests, nor the sourcecode for other JDK-versions.
Full source code, including tests and build files, can be obtained from the Subversion repository at SourceForge.net. The repository URL is
svn://svn.code.sf.net/p/firebird/code/client-java
Alternatively source code can be viewed online at http://firebird.svn.sourceforge.net/viewvc/firebird/client-java/

## Documentation and Support
### Where to get more information on Jaybird
The most detailed information can be found in the Jaybird Frequently Asked Questions (FAQ). The FAQ is included in the distribution, and is available on-line in several places.
JaybirdWiki is available at http://Jaybirdwiki.firebirdsql.org (note: this resource is out of date and will be discontinued in the near future)
Jaybird 2.1 Programmers Manual: http://www.firebirdsql.org/file/documentation/drivers_documentation/Jaybird_2_1_JDBC_driver_manual.pdf
### Where to get help
The best place to start is the FAQ. Many details for using Jaybird with various programs are located there. Below are some links to useful web sites.
- The http://groups.yahoo.com/group/Firebird-Java and corresponding mailing-list Firebird-Java@yahoogroups.com
- The code for Firebird and this driver are on http://sourceforge.net/projects/firebird
- The Firebird project home page http://www.firebirdsql.org
### Contributing
There are several ways you can contribute to Jaybird or Firebird in general:
- Participate on the mailinglists (see http://www.firebirdsql.org/en/mailing-lists/)
- Report bugs or submit patches on the tracker (see below)
- Become a developer (for Jaybird contact us on Firebird-Java, for Firebird in general, use the Firebird-devel mailing-list)
- Become a paying member or sponsor of the Firebird Foundation (see http://www.firebirdsql.org/en/firebird-foundation/)
See also http://www.firebirdsql.org/en/consider-your-contribution/
### Reporting Bugs
The developers follow the Firebird-Java@yahoogroups.com list. Join the list and post information about suspected bugs. List members may be able to help out to determine if it is an actual bug, provide a workaround and get you going again, whereas bug fixes might take awhile.
If you are sure that this is a bug you can report it in the Firebird bug tracker, project “Java Client (Jaybird)” at http://tracker.firebirdsql.org/browse/JDBC
When reporting bugs, please provide a minimal, but complete reproduction, including databases and sourcecode to reproduce the problem. Patches to fix bugs are also appreciated. Make sure the patch is against a recent trunk version of the code.
### Corrections/Additions To Release Notes
Please send corrections, suggestions, or additions to these Release Notes to to the mailing list at Firebird-Java@yahoogroups.com.

## JDBC URL Format
Jaybird provides different JDBC URLs for different usage scenarios:
### Pure Java
jdbc:firebirdsql://host[:port]/<database>
Default URL, will connect to the database using Type 4 JDBC driver using the Java implementation of the Firebird wire-protocol. Best suited for client-server applications with dedicated database server. Port can be omitted (default value is 3050), host name must be present.
The <database> part should be replaced with the database alias or the path to the database. In general it is advisable to uses database aliases instead of the path the file.
On Linux the root / should be included in the path. A database located on /opt/firebird/db.fdb should use the URL below (note the double slash after port!). jdbc:firebirdsql://host:port//opt/firebird/db.fdb
Deprecated but still available alternative URL:
jdbc:firebirdsql:host[/port]:<database>
### Using Firebird client library
jdbc:firebirdsql:native:host[/port]:<database>
Type 2 driver, will connect to the database using client library (fbclient.dll on Windows, and libfbclient.so on Linux). Requires correct installation of the client library.
jdbc:firebirdsql:local:<database>
Type 2 driver in local mode. Uses client library as in previous case, however will not use socket communication, but rather access database directly. Requires correct installation of the client library.
### Embedded Server
jdbc:firebirdsql:embedded:<database>
Similar to the Firebird client library, however fbembed.dll on Windows and libfbembed.so on Linux are used. Requires correctly installed and configured Firebird embedded library.
## Using Type 2 and Embedded Server driver
Jaybird 2.2 provides a Type 2 JDBC driver that uses the native client library to connect to the databases. Additionally Jaybird 2.2 can use the embedded version of Firebird so Java applications do not require a separate server setup.
However the Type 2 driver has its limitations:
Due to multi-threading issues in the Firebird client library as well as in the embedded server version, it is not possible to access a single connection from different threads simultaneously. When using the client library only one thread is allowed to access a connection at a time. Access to different connections from different threads is however allowed. Client library in local mode and embedded server library on Linux do not allow multithreaded access to the library. Jaybird provides necessary synchronization in Java code, however the mutex is local to the classloader that loaded the Jaybird driver.
Care should be taken when deploying applications in web or application servers: put jar files in the main library directory of the web and/or application server, not in the library directory of the web or enterprise application (WEB-INF/lib directory or in the .EAR file).
### Configuring Type 2 JDBC driver
The Type 2 JDBC driver requires the Jaybird JNI library to be installed and available to the Java Virtual Machine. Precompiled binaries for Windows and Linux platforms are distributed with Jaybird.
Please note that Jaybird 2.2 provides an update to the JNI libraries to support new features. It is not compatible with the JNI library for Jaybird 2.1 or earlier.
- jaybird22.dll / jaybird22_x64.dll is a precompiled binary for the Windows platform. It was successfully tested with Windows XP and Windows 7, but there should be no issues in other Win32 OS versions (as long as the MS Visual C++ 2010 SP1 distributable is available).
  The library should be copied into a directory in the PATH environment variable, or be made available to the JVM using the java.library.path system property.
- libjaybird22.so / libjaybird22_x64.so is a precompiled binary for the Linux platform (AMD/Intel). It must be available via the LD_LIBRARY_PATH environment variable, or be made available to the JVM using the java.library.path system property.
  Dependent libraries (libfbclient.so or libfbembed.so) need to be on the LD_LIBRARY_PATH. The java.library.path is ignored for these libraries as they are loaded from the JNI library, and not from Java.
  Some Firebird distributions will not create libfbclient.so (but only libfbclient.so.2 and .so.2.5), you will need to add a symlink with the name as expected by Jaybird.
- Other platforms can easily compile the JNI library by checking out the Jaybird sources from the CVS and using ./build.sh compile-native command in the directory with checked out sources.
After making Jaybird JNI library available to the JVM, the application has to tell driver to start using this by either specifying TYPE2 or LOCAL type in the connection pool or data source properties or using appropriate JDBC URL when connecting via java.sql.DriverManager.
### Configuring Embedded Server JDBC driver
The Embedded Server JDBC driver uses the same JNI library and configuration steps for the Type 2 JDBC driver.
There is however one issue related to the algorithm of Firebird Embedded Server installation directory resolution. Firebird server uses pluggable architecture for internationalization. By default server loads fbintl.dll or libfbintl.so library that contains various character encodings and collation orders. This library is expected to be installed in the intl/ subdirectory of the server installation. The algorithm of directory resolution is the following:
1. FIREBIRD environment variable.
2. RootDirectory parameter in the firebird.conf file.
3. The directory where server binary is located.
When Embedded Server is used from Java and no FIREBIRD environment variable is specified, it tries to find firebird.conf in the directory where application binary is located. In our case application binary is JVM and therefore Embedded Server tries to find its configuration file in the bin/ directory of the JDK or JRE installation. Same happens to the last item of the list. In most cases this is not desired behavior.
Therefore, if the application uses character encodings, UDFs or wants to fine-tune server behavior through the configuration file, the FIREBIRD environment variable must be specified and point to the installation directory of the Embedded Server, e.g. current working directory.
### Support for multiple JNI libraries
Up to Jaybird 2.0 only one client library could be loaded in a single JVM. That could be either an embedded Firebird library (fbembed.dll/libfbembed.so), or Firebird client library (fbclient.dll/libfbclient.so). This could lead to problems, For example, if embedded Firebird was used first, the JDBC driver would access the database file directly instead of using the local IPC protocol if only the path to the database was specified. It was not possible to change this without restarting the JVM.
Since Jaybird 2.1, Jaybird is able to correctly load arbitrary number of shared libraries that implement the ISC API and forward the requests correctly depending on the type of the driver being used.
## JDBC Compatibility
The Jaybird driver is not officially JDBC-compliant as the certification procedure is too expensive. The following lists some of the differences between JDBC specification and Jaybird implementation. This list is not exhaustive.
### JDBC deviations and unimplemented features
The following optional features and the methods for their support are not implemented:
- java.sql.Array data type is not (yet) supported
- java.sql.Blob does not implement following methods:
  - position(Blob, long) and position(byte[], long); Firebird does not provide any server-side optimization for these calls, client application must fetch complete BLOB content from the server to do pattern search.
  - truncate(long); Firebird does not provide such functionality on the server side, application must fetch old BLOB from the server and pump old content into a newly created BLOB.
- java.sql.Connection
  - getCatalog() and setCatalog(String) are not supported by Firebird server
  - getTypeMap() and setTypeMap(Map) are not supported
- java.sql.Ref data type is not supported by Firebird server
- java.sql.SQLData data type is not supported by Firebird server
- java.sql.SQLInput is not supported
- java.sql.SQLOutput is not supported
- java.sql.SQLXML is not supported
- java.sql.RowId is not supported
- java.sql.NClob is not supported
- java.sql.Statement
  - cancel() is implemented, but not fully supported by Jaybird
- java.sql.Struct data type is not supported by server.
The following methods are implemented, but deviate from the specification:
- java.sql.Statement
  - get/setMaxFieldSize does nothing, Firebird server does not support this feature.
  - get/setQueryTimeout does nothing, Firebird server does not support this feature.
- java.sql.PreparedStatement
  - setObject(int index, Object object, int type) Target SQL type is determined from the class of the passed object and corresponding parameter is ignored.
  - setObject(int index, Object object, int type, int scale) Same as above, type and scale are ignored.
- java.sql.ResultSetMetaData
  - isReadOnly() always returns false
  - isWritable() always returns true
  - isDefinitivelyWritable() always returns true
## Jaybird Specifics
Jaybird has some implementation-specific issues that should be considered during development.
### Result sets
Jaybird behaves differently not only when different result set types are used but also whether the connection is in auto-commit mode or not.
- ResultSet.TYPE_FORWARD_ONLY result sets when used in auto-commit mode are completely cached on the client before the execution of the query is finished. This leads to the increased time needed to execute statement, however the result set navigation happens almost instantly. When auto-commit mode is switched off, only part of the result set specified by the fetch size is cached on the client.
- ResultSet.TYPE_SCROLL_INSENSITIVE result sets are always cached on the client. The reason is quite simple – the Firebird API does not provide scrollable cursor support, navigation is possible only in one direction.
- ResultSet.HOLD_CURSORS_OVER_COMMIT holdability is supported in Jaybird only for result sets of type ResultSet.TYPE_SCROLL_INSENSITIVE. For other result set types driver will throw an exception.
### Using java.sql.ParameterMetaData with Callable Statements
This interface can be used only to obtain information about the IN parameters. Also it is not allowed to call the PreparedStatement.getParameterMetaData method before all of the OUT parameters are registered. Otherwise the corresponding method of CallableStatement throws an SQLException, because the driver tries to prepare the procedure call with incorrect number of parameters.
### Using ResultSet.getCharacterStream with BLOB fields
Jaybird JDBC driver always uses connection encoding when converting array of bytes into character stream. The BLOB SUB_TYPE 1 fields allow setting the character encoding for the field. However when the contents of the field is sent to the client, it is not converted according to the character set translation rules in Firebird, but is sent “as is”. When such fields are accessed from a Java application via Jaybird and character set of the connection does not match the character encoding of the field, conversion errors might happen. Therefore it is recommended to convert such fields in the application using the appropriate encoding.
### Heuristic transaction completion support
Current JCA implementation does not support XAResource.forget(Xid). It might be important in cases where a distributed transaction - that was at some time in-limbo - was either committed or rolled back by the database administrator. Such transactions appear to Jaybird as successfully completed, however XA specification requires resource manager to “remember” such transaction until the XAResource.forget(Xid) is called.
### Compatibility with com.sun.rowset.*
The reference implementation of javax.sql.rowset included with Java in package com.sun.rowset does not correctly look up columns by name as it ignores column aliases and only allows look up by the original column name[2] (this specifically applies to com.sun.rowset.CachedRowSetImpl).
[2] See JDBC-162 and http://bugs.sun.com/bugdatabase/view_bug.do?bug_id=7046875 for details
We advise you to either only access columns by their index or use an implementation which correctly uses the column label for column lookup (which is either the alias or the original column name if no alias was defined).